## Slide 1
NANOPORE PROJECT
Kraken2 Classification and
GPU-Accelerated Dorado Basecalling
Under the guidance of
Prof. Kolin Paul
Students
Chirag Kathpalia · Chirag Suthar

## Slide 2
HARDWARE
Experimental Machines
Hardware specs of machines we tested on, namely Luna (server) · Orion (edge) · Lab Desktop (Dell OptiPlex 5090)
 | Luna | Orion | Lab Desktop
Platform | Dell R760 (Server) | NVIDIA Jetson AGX Orin 64GB | Dell OptiPlex 5090
Architecture | x86_64 (Sapphire Rapids) | ARM64 (Cortex-A78AE) | x86_64 (Intel)
CPU | Intel Xeon Platinum 8468 | ARM Cortex-A78AE | Intel Core i7-11700 (11th Gen)
Cores / Threads | 96 cores / 192 threads | 12 cores / 3 clusters × 4 (no HT) | 8 cores / 16 threads (HT)
Clock | 3.8 GHz | 2.2 GHz | 2.50 GHz base / 4.90 GHz boost
NUMA Nodes | 2 | 1 | 1
SIMD | AVX-512 + AMX | NEON | AVX-512 (F/DQ/BW/VL/IFMA/VBMI/VNNI), AVX2, FMA
L1d Cache | 48 KB/core | 64 KB/core | 384 KiB (8×48 KiB)
L2 Cache | 2 MB/core | 256 KB/core | 4 MiB (8×512 KiB)
LLC (L3) | 210 MB total | 6 MB total (2 MB/cluster) | 16 MiB (shared, single instance)
Memory Type | DDR5, discrete | LPDDR5, unified (CPU+GPU share) | DDR4, discrete
RAM | 503 GB | 64 GB | 32 GB
GPU | 2× NVIDIA L40S (46 GB VRAM each) | Ampere, 2048 CUDA cores (integrated) | Intel UHD Graphics 750 (integrated)
01

## Slide 3
KRAKEN2 PROFILING
Where Does Kraken2 Spend Its Time?
Profiling done on Luna – for a 4 GB pod5 containing 104,918 reads, 703 MB HAC FASTQ, 8 GB standard database, 1 thread
CPU Time by Function (gprof, 1T)
MinimizerScanner::NextMinimizer
53.35%
CompactHashTable::Get
23.23%
ClassifySequence
7.27%
reverse_complement
6.69%
AddHitlistString
3.15%
Others
6.31%
CompactHashTable::Get() - The Hidden Bottleneck
0.65%
Share of Instructions
96.24%
Share of LLC Misses
The hidden bottleneck
Executes 0.65% of instructions - causes 96.24% of all LLC read misses.
Source: gprof (CPU time) + cachegrind (LLC miss attribution) | Luna, Xeon Platinum 8468, 8 GB Kraken2 standard database
02

## Slide 4
DORADO PROFILING
Dorado GPU Basecalling - Headline Finding
nsys profiling on Luna L40S | pod5_10, 104,918 reads
Model | Architecture | Top GPU Consumer
fast | LSTM (small) | GEMM 30.8%
hac | LSTM (large) | LSTM 68.0%
sup | Transformer + FP8 | RMSNorm 17.1% + FP8-GEMM 43.6%
sup is architecturally different - not just “bigger”
sup is a Transformer (like GPT), not an RNN at all. It uses FP8 quantization, an Ada Lovelace-native feature. That's why batch size collapses to 96 - the model is massive - and the CPU is almost constantly blocked waiting on the GPU.
Each model has a genuinely different dominant kernel - there is no single “where Dorado spends its time” answer across models.
03

## Slide 5
DORADO PROFILING
GPU Kernel Breakdown by Model
nsys profiling on Luna L40S (Ada Lovelace, 91.6 TFLOPS FP32) | 104,918 reads, same pod5 input across all models
Chart: 
| fast (LSTM, FP16) | hac (LSTM large, FP16) | sup (Transformer, FP8)
GEMM | 30.8 | 15 | 43.6
LSTM | 27.5 | 68 | 0
Beam Search | 14.8 | 2.1 | 8.5
Attention | 0 | 0 | 10.4
RMSNorm | 0 | 0 | 17.1
Other | 26.9 | 14.9 | 20.4
GEMM = matmul kernels. sup splits its time across five distinct kernel types - fast and hac are dominated by one or two.
04

## Slide 6
DORADO PROFILING
GPU Speedup vs CPU (log scale)
Same model, same input - Luna 2× L40S vs Luna CPU (96 cores)
10s
1min
5min
33.9s
Luna GPU
28.6× vs CPU
fast
55.0s
Luna GPU
107× vs CPU
hac
4.4m
Luna GPU
~3,000× vs CPU
sup
CPU falls back to FP32 - no native FP8 on Xeon
sup's ~3,000× speedup is driven by FP8 tensor-core acceleration that simply doesn't exist on the CPU side - not just raw parallelism.
Wall times shown are Luna GPU only. Full CPU vs GPU vs Orion comparison is on the next chart.
05

## Slide 7
DORADO PROFILING
Dorado - Full Model Comparison
Luna L40S | pod5_10, 104,918 reads | dorado v1.4.0
Model | Architecture | Precision | GEMM% | LSTM% | Beam% | Attn% | RMSNorm% | Wall time | GPU vs CPU | CPU sync-blocked
fast | LSTM | FP16 | 30.8% | 27.5% | 14.8% | 0% | 0% | 33.9s | 28.6× | 96.5%
hac | LSTM (large) | FP16 | 15.0% | 68.0% | 2.1% | 0% | 0% | 55.0s | 107× | 96.1%
sup | Transformer | FP8+FP16 | 43.6% | 0% | 8.5% | 10.4% | 17.1% | 4m 26s | ~3,000× | 98.7%
CPU sits idle-blocked 96–99% of the time across all three models
“Sync-blocked” = cudaStreamSynchronize + cudaEventSynchronize time. This means the GPU - not the CPU - always drives the pipeline. Even the “lightest” model (fast) leaves the CPU waiting 96.5% of wall time.
Source: nsys 2025.1.3 | Luna L40S | Dorado v1.4.0 | models dna_r10.4.1_e8.2_400bps_v5.2.0
06

## Slide 8
DATABASE DESIGN
Kraken2 Database Hierarchy - Accuracy vs Cache Pressure
6 databases tested - ultra-targeted (6 genomes) to gold-standard (RefSeq + fungi/protozoa) | reads_hac, 32T, Luna
Database | Hash Table Size | Contents | Classification Accuracy | LLC Miss Rate
sample_targeted | 50 MB | 6 reference genomes (exact sample match) | 84.80% | 14.64%
eskape_650mb | 142 MB | ESKAPE pathogens only (1,149 assemblies) | 65.28% | 30.53%
eskape_human_4gb | 3.8 GB | ESKAPE + human genome (GRCh38) | 66.13% | 59.03%
standard_8gb | 7.6 GB | Bacteria + archaea + viral + plasmid + human | 95.77% | 82.90%
standard_16gb | 15 GB | Same as above, larger cap | 97.77% | 85.03%
pluspf_103gb | 103.4 GB | Standard + protozoa + fungi (full RefSeq) | 98.86% | 91.13%
● Pre-cliff ● Bandwidth-saturated ● Amdahl-limited
As databases scale up
Accuracy rises (more organisms to match) but LLC miss rate rises too (more DRAM accesses per k-mer lookup). The 50 MB → 142 MB step crosses the cache cliff - LLC miss rate jumps from ~15% to ~31%. Luna's LLC is 210 MB; every database beyond sample_targeted exceeds effective cache capacity.
07

## Slide 9
DATABASE DESIGN
Custom 50 MB DB vs Gold-Standard 103 GB DB
Classification rate | reads_hac, 32T, Luna | 104,918 reads total
Chart: 
| sample_targeted (50 MB) | pluspf_103gb (103 GB)
Classified | 84.8 | 98.86
Unclassified | 15.2 | 1.14
The 50 MB custom DB misses 15% of reads entirely. The 103 GB gold-standard classifies 98.86% - species breakdown on next slide.
08

## Slide 10
DATABASE DESIGN
Species Composition - Same Sample, Different Picture
% of all reads | reads_hac, 32T, Luna | 104,918 reads total
Chart: 
| P. aeruginosa | E. coli | K. pneumoniae | A. baumannii | Other classified | Unclassified
50 MB DB | 52.5 | 21.79 | 9.92 | 0 | 0.59 | 15.2
103 GB DB | 41.58 | 20.6 | 9.22 | 0.33 | 26.86 | 1.14
A. baumannii - invisible to the 50 MB DB
0% vs 0.33% - an ESKAPE pathogen, completely absent from the custom DB (NCBI genome suppressed).
The 27% long tail
“Other classified” jumps from 0.59% to 26.86% - the 103 GB DB reveals a large microbial long tail that's structurally invisible to any narrow, targeted database, no matter how well-tuned.
09

## Slide 11
THREAD SCALING
Thread Scaling - Luna (Xeon Platinum 8468, 96c)
Speedup vs thread count | reads_hac · numactl --cpunodebind=0 --membind=0 · 6 databases
Chart: Thread count
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 96
50 MB (pre-cliff) | 1 | 1.98 | 3.89 | 7.52 | 13.9 | 21.26 | 20.83 | 17.85
142 MB (bw-sat.) | 1 | 1.97 | 3.85 | 7.37 | 13.45 | 21.03 | 21.96 | 18.88
3.8 GB (bw-sat.) | 1 | 1.87 | 3.33 | 5.43 | 7.93 | 10.02 | 10.57 | 10.12
7.6 GB (Amdahl) | 1 | 1.59 | 2.26 | 2.87 | 3.29 | 3.47 | 3.39 | 3.28
15 GB (Amdahl) | 1 | 1.51 | 2.04 | 2.49 | 2.79 | 2.93 | 2.9 | 2.85
103 GB (DRAM-sat.) | 1 | 1.28 | 1.47 | 1.6 | 1.67 | 1.71 | 1.71 | 1.72
32T sweet spot
5 of 6 databases peak at 32 threads. The 103 GB DB alone keeps climbing to 96T - it's DRAM-saturated, never compute-bound, so more threads keep helping.
Ideal linear reference
A perfectly parallel workload would show 32× speedup at 32 threads. Only the 50 MB and 142 MB databases get close (21–22×) - everything larger is bottlenecked well before that ideal.
10

## Slide 12
THREAD SCALING
Thread Scaling - Luna: Key Metrics
reads_hac, key thread counts (1T and 32T) across all 6 databases
Database | 1T Time (s) | 32T Time (s) | Peak Speedup | LLC Miss % | IPC (1T)
50 MB sample_targeted | 19.7 | 0.93 | 21.3× @32T | 10.2% | 1.78
142 MB eskape_650mb | 22.0 | 1.05 | 22.0× @64T | 30.7% | 1.47
3.8 GB eskape_human_4gb | 29.8 | 2.98 | 10.6× @64T | 56.9% | 1.25
7.6 GB standard_8gb | 16.8 | 4.83 | 3.5× @32T | 76.6% | 2.11
15 GB standard_16gb | 23.9 | 8.15 | 2.9× @32T | 80.2% | 1.86
103 GB pluspf_103gb | 96.9 | 56.8 | 1.72× @96T | 90.5% | 1.00
IPC collapses under DRAM pressure
At 103 GB / 96T, IPC drops to 0.90 - more stall cycles than executed instructions. LLC Miss% rises with thread count on every database, since more concurrent threads means more simultaneous DRAM pressure.
11

## Slide 13
THREAD SCALING
Thread Scaling - Orion (Jetson AGX Orin, 12c ARM)
Speedup vs thread count | reads_hac · sudo perf · 5 databases (103 GB DB does not fit 64 GB RAM)
Chart: Thread count
| 1 | 2 | 4 | 6 | 8 | 10 | 12
50 MB (post-cliff) | 1 | 2.03 | 4.02 | 5.97 | 7.91 | 9.64 | 11.44
142 MB | 1 | 2.02 | 3.97 | 5.91 | 7.82 | 9.58 | 11.34
3.8 GB | 1 | 1.98 | 3.75 | 5.37 | 6.89 | 8.18 | 9.39
7.6 GB (Amdahl floor) | 1 | 1.91 | 3.14 | 4.02 | 4.65 | 5.16 | 5.54
15 GB (Amdahl floor) | 1 | 1.76 | 2.78 | 3.42 | 3.87 | 4.22 | 4.5
50 MB and 142 MB overlap
On Orion BOTH are post-cliff (SLC = 6 MB) - DB size stops changing miss rate once you're past the cliff.
35× smaller cache than Luna
Orion's SLC is 6 MB vs Luna's 210 MB. That makes the 50 MB DB - pre-cliff on Luna - behave like a large, post-cliff database on ARM.
12

## Slide 14
THREAD SCALING
Thread Scaling - Orion: Key Metrics
reads_hac, 1T and 12T across all 5 databases
Database | 1T Time (s) | 12T Time (s) | Peak Speedup | LLC Miss %(1T) | IPC (1T)
50 MB sample_targeted | 47.5 | 4.15 | 11.4× @12T | 78.9% | 1.00
142 MB eskape_650mb | 47.1 | 4.15 | 11.3× @12T | 80.8% | 0.93
3.8 GB eskape_human_4gb | 45.8 | 4.88 | 9.4× @12T | 77.3% | 1.07
7.6 GB standard_8gb | 21.2 | 3.82 | 5.5× @12T | 68.2% | 2.24
15 GB standard_16gb | 28.4 | 6.32 | 4.5× @12T | 71.4% | 1.92
Why is standard_8gb faster than 50 MB at 1T?
21.2s vs 47.5s - a different k-mer lookup pattern: the standard DB terminates lookups earlier with more successful matches (IPC 2.24 vs 1.00). All DBs are post-cliff on Orion, so classification efficiency - not DB size - drives wall time here.
13

## Slide 15
THREAD SCALING
Lab Desktop: Kraken2 Thread Scaling (Dell OptiPlex 5090)
Intel i7-11700 · 8 physical cores / 16 HT · 16 MB L3 · reads_hac × threads 1,2,4,8,16
Chart: Thread count
| 1 | 2 | 4 | 8 | 16
eskape_51mb (51 MB) | 1 | 1.93 | 3.52 | 5.35 | 7.57
eskape_650mb (142 MB) | 1 | 1.92 | 3.49 | 5.55 | 8.11
standard_8gb (7.6 GB) | 1 | 1.63 | 2.44 | 3.07 | 3.37
standard_16gb (15 GB) | 1 | 1.52 | 2.04 | 2.42 | 2.51
8-core physical ceiling
8T = the physical core count. Beyond that, gains come only from hyperthreading - a fundamentally different regime.
HT: +46% for small DBs
eskape_650mb: 5.55× (8T) → 8.11× (16T). Latency-bound workloads benefit most from HT.
HT: +4% for large DBs
standard_16gb: 2.42× (8T) → 2.51× (16T). HT is nearly useless once bandwidth-bound.
14

## Slide 16
THREAD SCALING
Lab Desktop - Full Thread Scaling Data
All databases × all thread counts (reads_hac)
Database | 1T time | 8T speedup | 16T speedup | LLC Miss% (1T) | IPC (1T) | Classified%
eskape_51mb (51 MB) | 17.8s | 5.35× | 7.57× | 52.6% | 1.43 | 84.80%
eskape_650mb (142 MB) | 18.2s | 5.55× | 8.11× | 56.5% | 1.30 | 65.28%
eskape_human_4gb (3.8 GB) | 21.8s | 4.76× | 6.42× | 72.5% | 1.20 | 66.13%
standard_8gb (7.6 GB) | 11.5s | 3.07× | 3.37× | 63.3% | 2.17 | 95.77%
standard_16gb (15 GB) | 18.0s | 2.42× | 2.51× | 69.1% | 1.81 | 97.77%
3-run averages, single NUMA node (no numactl needed), warmup discarded. eskape_51mb = custom 6-genome ESKAPE panel.
15

## Slide 17
THREAD SCALING
Lab Desktop - Key Observations
8-core Rocket Lake, 16 MB L3 - what the numbers reveal
8-core ceiling
Speedup saturates at 8T for bandwidth-bound DBs (standard_8gb: 3.07×). Hyperthreading adds only ~10% more for large DBs - 8 physical cores already saturate DRAM bandwidth.
HT pays off for small DBs
eskape_650mb: 5.55× (8T) → 8.11× (16T) = +46%. Small DBs are latency-bound, not bandwidth-bound - the 2nd hyperthread hides memory stall of the 1st. Same pattern in eskape_51mb (+42%) and eskape_human_4gb (+35%).
IPC tells the real story
standard_8gb IPC = 2.17 despite 63% LLC miss rate - repetitive k-mers pipeline well (high MLP). eskape_human_4gb IPC = 1.20 despite similar miss rate - diverse k-mer space serializes misses. Miss rate alone doesn't predict throughput.
Custom 51 MB DB beats 650 MB DB by +19pp
eskape_51mb classified 84.80% vs eskape_650mb's 65.28% - because it carries dedicated references for P. aeruginosa, E. coli, K. pneumoniae (this sample's dominant organisms). eskape_650mb classifies E. coli and K. pneumoniae reads as zero. Targeted panel wins on this sample.
Machine: Dell OptiPlex 5090 · i7-11700 · 8C/16T · 16 MB L3 · 32 GB RAM · Ubuntu 22.04.5 LTS. Databases on local disk; reads_hac (104,918 reads, 355 Mbp). Data from Chirag Suthar (hobbbit branch).
16

## Slide 18
VALIDATION
GPU Throughput Is Input-Size-Invariant
All 16 FBE pod5 files merged → 1,865,971 reads · Luna L40S · 2026-06-29
Chart: sp/s (×10⁶)
| fast | hac | sup
Single pod5 (104,918 reads) | 235 | 203 | 19.79
Merged all 16 (1,865,971 reads) | 234.5 | 211.4 | 19.79
Model | Single wall | Merged wall | Scale factor
fast | 33.9s | 5m 43.5s | 17.85×
hac | 55.0s | 6m 21.1s | 17.85×
sup | 4m 26s | 67m 50.8s | 17.85×
Throughput differs by < 1%
L40S is always maximally utilized - single-file benchmarks (like slides 4–6) are fully representative of full-dataset behavior.
Single pod5 baseline = pod5_10. Merged = all 16 pod5 files via dorado directory input (pod5 merge v0.3.39 skipped - corrupted zstd blocks). 25 reads in pod5_9 skipped due to pre-existing disk corruption (0.001%).
17

## Slide 19
VALIDATION
32-Thread Parallelism Absorbs 17.85× More Reads
Kraken2 wall time, LLC miss%, classification% - single (104,918 reads) vs merged (1,865,971 reads)
50 MB DB (fits in LLC)
Run | Wall | LLC% | Class.%
Single hac (104,918) | 4.41s | 14.64% | 84.80%
Merged fast (1,865,971) | 11.11s | 12.60% | 80.67%
Merged hac (1,865,971) | 11.10s | 13.11% | 84.73%
Merged sup (1,865,971) | 12.18s | 12.26% | 85.46%
103 GB DB (DRAM-bound)
Run | Wall (warm) | LLC% | Class.%
Single hac (104,918) | 56.76s | 91.13% | 98.86%
Merged fast (1,865,971) | 89.24s | 75.44% | 96.53%
Merged hac (1,865,971) | 79.97s | 73.73% | 98.83%
Merged sup (1,865,971) | 77.31s | 73.27% | 99.32%
Kraken2 scales sub-linearly
17.85× more reads → only 2.52× more time (50 MB DB). 32-thread parallelism absorbs the input growth. Per-read cost drops as thread utilization increases.
LLC miss rate is DB-driven
50 MB DB: ~13% miss rate regardless of read count. 103 GB DB: ~73–75%. Cache behavior tracks database structure, not dataset size.
Dorado GPU throughput invariant
L40S processes signal at a constant rate regardless of input size (see previous slide) - single-file benchmarks are fully representative.
18

## Slide 20
DORADO PROFILING
Dorado: GPU Acceleration vs CPU Baseline
Luna L40S GPU vs Luna CPU vs Orion Ampere iGPU · pod5_10 (104,918 reads) · log-scale runtimes
10s
1min
10min
1hr
1day
9days
33.9s
Luna GPU
L40S: 28.6× vs CPU
6.7m
Orion GPU
Orion: 1.4× vs CPU
9.7m
Luna CPU
fast
55.0s
Luna GPU
L40S: 107× vs CPU
1.0d*
Orion GPU
Orion: est. ~30×*
43.4m
Luna CPU
hac
4.4m
Luna GPU
L40S: ~3,000× vs CPU (est.)
not run
Orion GPU
9.0d*
Luna CPU
sup
* Dashed bars = estimates. Orion HAC: ~1 day from progress bar before SSH disconnect. Luna CPU SUP: ~9 days from progress bar at 12 min; run cancelled. Orion SUP not run (impractical).
19

## Slide 21
DORADO PROFILING
Kernel Architecture Changes With Each Model
% of total GPU time by kernel category - Luna L40S, nsys
Kernel category | fast | hac | sup
LSTM kernels | 27.5% | 68.0% | 0%
GEMM (matrix multiply) | 30.8% | 15.0% | 43.6%
Beam search (CTC decode) | 14.8% | 2.1% | 8.5%
Transformer ops (attn, RMSNorm, FP8) | 0% | 0% | ~28%
Other | 26.9% | 14.9% | 19.9%
sup runs on fundamentally different hardware paths
sup uses FP8 tensor cores (fp8_e4m3) - no CPU architecture supports native FP8. That single fact drives the ~3,000× GPU advantage seen on the previous chart.
The FP8 problem
CPUs have no native FP8 support → dorado falls back to FP32 for every FP8 op. Luna's Xeon Platinum 8468 has AMX for BF16/INT8 - not FP8. Fused GPU kernels (e.g. mm_swiglu<fp8> = matmul + SwiGLU in one pass) split into separate CPU ops. Result: an estimated 9-day CPU runtime vs 4m 26s on GPU.
20

## Slide 22
DORADO PROFILING
L40S Nearly Fully Occupied
GPU utilization summary - CUDA API sync time, batch size, throughput
Metric | fast | hac | sup
GPU time blocked in sync | 96.5% | 96.1% | 98.7%
Batch size on L40S | 320 | 2,944 | 96 (VRAM-limited)
Throughput (sp/s) | 2.35×10⁸ | 2.03×10⁸ | 1.98×10⁷
GPU-paced, not CPU-paced
96–99% of CUDA API time is cudaStreamSynchronize / cudaEventSynchronize - the CPU sits idle waiting for the GPU. Dorado is entirely GPU-paced. Orion is limited to batch=64 (unified memory constraint), which explains its slower speedup relative to Luna.
Input: FBE01990_24778b97_03e50f91_10.pod5 (104,918 reads). Luna GPU: 2× NVIDIA L40S 46GB Ada Lovelace, dorado v1.4.0. Luna CPU: 96-core Xeon Platinum 8468, ~130 cores active. Orion: 2048-core Ampere iGPU, dorado v0.5.3, batch=64. nsys 2025.1.3.
21

## Slide 23
DORADO PROFILING
CPU vs GPU: Why the Gap Compounds
Model-to-model slowdown - Luna GPU vs Luna CPU
Step | Luna GPU | Luna CPU | CPU penalty growth
fast → hac | 1.62× slower | 4.5× slower | 2.8× larger
hac → sup | 4.84× slower | ~298× slower | ~62× larger
fast → sup (total) | 7.85× slower | ~1,340× slower | 171× larger
Batch sizes: fast GPU=320, hac GPU=2,944, sup GPU=96 (VRAM-limited by Transformer size). Orion GPU capped at batch=64 across all models (unified memory constraint).
Why SUP CPU takes ~9 days
No CPU architecture supports FP8. Xeon Platinum 8468 falls back to FP32 for every FP8 op. Fused GPU kernels split into separate CPU operations - the penalty compounds with every architectural improvement.
Why Orion lags for hac/sup
Ampere iGPU (2,048 cores) vs Ada Lovelace (18,176 CUDA + 568 tensor cores). Batch size capped at 64 (OOM at default) - underutilizes the GPU. HAC: ~1 day on Orion vs 55s on Luna.
Clinical implication
SUP gives 99.3% classification accuracy (vs 84.7% for fast on the 50 MB DB). On CPU that takes ~9 days per run. On Luna L40S: 4m 26s. GPU is not optional for clinical-grade nanopore diagnostics.
22

## Slide 24
HASH TABLE DESIGN
Cell-Width Reduction: Can We Halve the Hash Table?
Modified Kraken2 source - CompactHashCell16 + CompactHashCell24 · ESKAPE 6-genome DB · 1,872,777 reads
Exact 2× size reduction - no other change
Cell width | key/val bits | hash.k2d size | vs 32-bit
32-bit (current) | 26 / 6 | 48.80 MB | 1.00× baseline
24-bit | 18 / 6 | 36.60 MB | 0.75× (−25%)
16-bit | 10 / 6 | 24.40 MB | 0.50× (HALF)
16-bit works - but ONLY with a confidence threshold
No threshold (-T 0) - false positives flood in
Model | 32-bit | 24-bit | 16-bit
fast | 67.70% | 68.15% | 88.82%
hac | 73.10% | 73.43% | 90.39%
sup | 73.85% | 74.14% | 90.37%
With threshold (-T 0.05) - fully converged (confidence score 5%)
Model | 32-bit | 24-bit | 16-bit
fast | 53.65% | 53.65% | 54.27%
hac | 61.47% | 61.47% | 61.76%
sup | 62.45% | 62.45% | 62.78%
-T 0.05 collapses the +21% false-positive flood down to +0.3–0.6% - 24-bit needs no threshold at all, matching 32-bit exactly (Δ=0).
23

## Slide 25
HASH TABLE DESIGN
Cross-Phylum Inflation Proves Hash Collisions
Reads out of 1,872,777 - 32-bit vs 16-bit, no threshold
Species | 32-bit reads | 16-bit reads | Inflation
P. aeruginosa | 983,897 | 1,061,599 | ×1.08
K. pneumoniae | 260,236 | 303,565 | ×1.17
E. cloacae | 116,195 | 194,795 | ×1.68
A. baumannii | 1,617 | 40,301 | ×25
S. aureus | 902 | 23,877 | ×26
E. faecium | 3 | 21,355 | ×7,118
Pure hash collision proof
E. faecium ×7,118 - this species shares zero 31-mers with the Gram-negative bacteria dominating this sample. All ~316k “new” reads come directly out of Unclassified. key_bits=10 means 1/1024 false-positive chance per minimizer lookup; long reads carry hundreds of minimizers, so spurious hits accumulate.
The Size-vs-Safety Dial
Width | Size | Threshold? | Verdict
32-bit | 48.80 MB | not needed | Current baseline
24-bit | 36.60 MB | not needed | Best trade-off - drop-in
16-bit | 24.40 MB | -T ≥ 0.05 | 50% smaller, clinically equivalent after threshold
Cache impact
The 16-bit ESKAPE DB (24.4 MB) sits deeper inside Luna's 210 MB LLC - every k-mer lookup stays in cache. 32-bit (48.80 MB) was already pre-cliff; 16-bit improves further still.
24-bit is the recommended default: 25% smaller with zero workflow change. 16-bit is available for memory-constrained deployments that can tolerate the -T flag requirement.
24

## Slide 26
Thank You
Nanopore Project · Prof. Kolin Paul
Chirag Kathpalia · Chirag Suthar